## Slide 1: Input output
Er. Deeyoranjan Dongol

## Slide 2: I/O MANAGEMENT
All computers have physical devices for acquiring input and producing output
OS is responsible to manage and control all I/O operations and I/O devices
Some principles I/O hardware
  I/O Devices
  I/O Controllers
  Memory mapped I/O
  DMA
  I/O Handling

## Slide 3: I/O DEVICES
A I/O units which consists of mechanical components are called I/O devices such as hard-disk drive, mouse
There are two types of devices
  Block Devices [Disk]
    Stores information in fixed sized blocks
    Each one with its own address
    Read/Write is possible independently
  Character Devices [Printer]
    Delivers or accepts a stream of characters without regard to any block structure
    Not addressable

## Slide 4: DEVICE CONTROLLERS
A controller is a collection of electronic component that can operate a bus or a device
A single controller can handle multiple devices but some devices have their own built-in controller
The controller has one or more registers for data and signals; processor communicates with controller by reading and writing bit patterns in these registers

## Slide 5: MEMORY-MAPPED I/O
The device control registers are mapped into memory space called memory-mapped I/O
Usually the assigned addresses are at the top of the address space

## Slide 6: MEMORY-MAPPED I/O
When a CPU wants to read a word either from memory or from I/O port, it puts the address it needs on the bus’s address line and then asserts the read signals on bus’s control line
A second signal is used to tell whether I/O or memory space is needed

## Slide 7: I/O HANDLING
Programmed I/O (Polling)
  Processing is interrupted at brief intervals to allow the CPU to check back to I/O to see if the I/O operations has completed
  Used in embedded system
Interrupt-Driven I/O
  The hardware mechanism that enables a device to notify the CPU
  Interrupt forces to stop CPU what it is doing and start doing something else
I/O Using DMA

## Slide 8: I/O HANDLING
Scenario: a cook is cooking something in modern microwave oven equipped kitchen
  CASE A: The cook may regularly peek through the oven’s glass door and watch as roast cooks under cook and watch; this kind of monitoring is polling
  CASE B: The cook may set a timer to expire after as appropriate number of minutes; the buzzer sounding after this interval is an interrupt

## Slide 9: DIRECT MEMORY ACCESS [DMA]

## Slide 10: DIRECT MEMORY ACCESS[DMA] WORKS
The CPU programs the DMA controller by its register so it knows what to transfer where. It also issues a command to disk controller telling it to read data from disk to its internal buffer and verify the checksum. When valid data are in disk’s controller buffer, DMA can begin
The DMA controller initiates the transfer by issuing a read request over the bus to disk controller
Data transferred from disk controller to memory
When transferred completed, the disk controller sends an acknowledgement signal to DMA controller. The DMA controller then increments the memory address and decrements the byte count. This continues until byte count reaches 0
When transfer completed the DMA controller interrupt the CPU

## Slide 11: I/O SOFTWARE ISSUES (GOALS OF I/O SOFTWARE)
Device Independence
Uniform Naming
Error Handling
Synchronous Vs Asynchronous transfer
Buffering

## Slide 12: I/O SOFTWARE LAYERS

## Slide 13: I/O SOFTWARE LAYERRS
Interrupt Handlers
  Block the driver until the I/O has completed and the interrupt occur
  The interrupt handler determines the cause of the interrupt and performs the necessary processing
    Save any registers that have not already been saved by the interrupt hardware
    Set up stack for interrupt service procedure
    Ack interrupt controller
    Copy registers from where they were saved to the process table
    Run the interrupt service procedure
    Set up the MMU context for the process to run next
    Load new process’s registers
    Start running the new process

## Slide 14: I/O SOFTWARE LAYERRS
Device Drivers
  Each I/O device attached to a computer needs some device-specific code for controlling it called device driver
  Generally written by device manufacturer and delivered along with the device
  Each device driver normally handles one device type or at most one class of closely related devices
  Functions:
    Accept read write requests from the device independent software above it
    Manage power requirement and log events
    Checks the status of devices in use or free

## Slide 15: I/O SOFTWARE LAYERRS
Device Independent OS software
  The devices independent software is to perform the I/O functions that are common to all devices and to provide a uniform interface to the user-level software
  Functions:
    Uniform interfacing for devices
    Buffering
    Error reporting
    Allocating and releasing dedicated devices
    Providing a device independent block size

## Slide 16: I/O SOFTWARE LAYERRS
User Processes
  System calls including the I/O system calls are normally made by the user processes
  User processes put their parameters in the appropriate place for the system calls or other procedures that actually do real work

## Slide 17
DISKS

## Slide 18
Disks come in many sizes and speeds and information may be stored optically or magnetically
    Example:- floppy disks, hard disks, CD-ROMS and DVDS
Disk surface is divided into number of logical block called sectors and tracks
The term cylinder refers to all the tracks at particular head position in hard disk

## Slide 19
Disk Structure

## Slide 20
Latency Time
    Time taken to rotate from its current position to a position adjacent to the read-write head
Seek
    The processes of moving the arm assembly to new cylinder
    To access a particular record, first the arm assembly must be moved to the appropriate cylinder and then rotate the disk until it is immediately under the read-write head.
    The time to access the whole record is called transmission time

## Slide 21
OS is responsible to use the hardware efficiently i.e. fast seek, latency and transmission time
For most disks, the seek time dominates the other two, so reducing the mean seek time can improve system performance
Consider a disk queue with requests for I/O to blocks on cylinders 98, 183, 41, 122, 14, 124, 65, 67. The head is initially at cylinder number 53 moving towards larger cylinder numbers on its servicing pass. The cylinders are numbered from 0 to 199. Calculate the total head movement for FCFS, SSTF, SCAN,C-SCAN, LOOK and C-LOOK Disk scheduling algorithm.

## Slide 22: DISK SCHEDULING
First-Come-First-Serve(FCFS)
  The first request to arrive is the first one serviced
  Advantage: Simple and easy to implement
  Problem: Does not provide fast service

## Slide 23: DISK SCHEDULING
First-Come-First-Serve(FCFS)
  Total head movement = 632 cylinders

## Slide 24: DISK SCHEDULING
Shortest-Seek-Time-First(SSTF)
  Selects the request with the minimum seek time from the current head position
  Advantage: Improved Performance
  Problem: SSTF is a form of SJf scheduling and may cause starvation of some requests

## Slide 25: DISK SCHEDULING
Shortest-Seek-Time-First(SSTF)
  Total head movement = 236 cylinders

## Slide 26: DISK SCHEDULING
SCAN
  The disk arm starts at one end of the disk and moves toward the other end, servicing requests until it gets to the other end of the disk, where head movement is reversed and servicing continues
  Sometimes called elevator algorithm
  Advantage: Decreases variances in seek and improve response time
  Problem: Starvation possible if there are repeated request in current track

## Slide 27: DISK SCHEDULING
SCAN
  Total head movement = 331 cylinders

## Slide 28: DISK SCHEDULING
C-SCAN
  The head moves from one end of the disk to the other servicing requests as it goes. When it reaches the other end, however, it immediately returns to the beginning of the disk, without servicing any requests on the return trip

## Slide 29: DISK SCHEDULING
C-SCAN
  Total head movement = 386 cylinders

## Slide 30: DISK SCHEDULING
LOOK
  Head starts from the first request at one end of the disk and moves towards the last request at the other end servicing all the requests in between
  After reaching the last request at the other end, head reverses its direction
  Returns to the first request at the starting end servicing all the requests in between

## Slide 31: DISK SCHEDULING
LOOK
  Total head movement = 299 cylinders

## Slide 32: DISK SCHEDULING
C-LOOK
  Head starts from the first request at one end of the disk and moves towards the last request at the other end servicing all the requests in between
  After reaching the last request at the other end, head reverses its direction
  Returns to the first request at the starting end without servicing any requests in between

## Slide 33: DISK SCHEDULING
C-LOOK
  Total head movement = 326 cylinders

## Slide 34: DISK FORMATTING
  Disk Formatting
    Before a disk can store data, it must be divided into sectors that the disk controller can read and write called low-level formatting
    The sector typically consists of
      Preamble:- Contains cylinder and sector number
      ECC:- Contains redundant information that can be used to recover from read error

## Slide 35: DISK FORMATTING

## Slide 36: DISK FORMATTING
  If disk I/O operations are limited to transferring a single sector at a time, it reads the first sector from the disk and doing ECC calculation transfers data to main memory, during this time the next sector will fly by the head
  When transferring completes the controller will have to wait almost an entire rotation for the second sector to come around again
  This problem can be eliminated by numbering the sectors in an interleaved fashion when formatting the disk
  According to copying rate, interleaving may be of single or double

## Slide 37: DISK FORMATTING

## Slide 38: ERROR HANDLING
  Most frequently, one or more sectors becomes defective or most disks even come from factory with bad blocks
  Depending on the disk and controller in use, these blocks are handled in variety of ways
    Bad blocks are handled manually
      Run MS-DOS chkdsk – find bad block
      Format command to create new block
    Using bad block recovery
      Controller maintains the list of bad blocks on the disk and substituted with spare

## Slide 39: ERROR HANDLING

## Slide 40
  RAID (Redundant Array of Inexpensive Disks)
    Issues: Disk Performance, Amount of Storage required and Reliability
    A technique of organizing multiple disks to address above issues is RAID
    RAID allows more than one disk to be used for a given operation and allows continued operation and even automatic recovery in the face of disk failure
    There are six types of organization called RAID levels

## Slide 41: RAID LEVELS
  RAID Level 0
    Creates one large virtual disk from a number of smaller disks
    Storage is grouped into logical units called strips
    Virtual storage is sequence of strips interleaved among the disks in the array
    Advantage
      Can create large disk
      Performance benefit can be achieved
    Disadvantage
      Reliability decrease

## Slide 42: RAID LEVELS
  RAID Level 1
    Stores duplicate copy of each strip with each copy on a different disk
    Advantage
      Excellent reliability; if drive crashes the copy is used
      Read performance can be achieved
    Disadvantage
      Write performance is no better than in single drive

## Slide 43: RAID LEVELS
  RAID Level 2
    An error-correcting code is used for corresponding bits on each data disks
    Error-correcting code scheme stores two or more extra bits and can reconstruct the data if a single bit get damaged
    Advantage
      Total parallelism
    Disadvantage
      Requires substantial number of drives
Notes: For Example, the first bit of each byte is stored in disk 1, second bit in disk 2, and until eight bit in disk 8, and error correcting bits are stored in further disks. If one of the disk fail, the remaining bits of the byte and associated error-correction bits can be read from other disks and be used to reconstruct the damage data.

## Slide 44: RAID LEVELS
  RAID Level 3
    Simplified version of level 2
    A single parity bit is used instead of error-correcting code, hence requires just one extra disk
    If any disk in array fails, its data can be determined from the data on the remaining disks
    It is as good as level 2 but is less expensive in the number of extra disks

## Slide 45: RAID LEVELS
  RAID Level 4
    It uses block-level striping as in level 0, and in addition keeps a parity block on separate disk for corresponding blocks from other disks
    If one of the disks fails, the parity block can be used with the corresponding blocks from other disks to restore the blocks of the fail disks
    To compute parity, simple function XOR is used For a given set of bits, the XOR of all of those bits returns a 0 if there are an even number of 1’s in the bits, and a 1 if there are an odd number of 1’s
    Problem: performance bottleneck

## Slide 46: RAID LEVELS
  RAID Level 5
    Similar to level 4 but parity information is distributed in all disks
    For each block one of the disk stores parity and other stores data

## Slide 47: STABLE STORAGE
  Major functions
    Stable Writes
    Stable Read
    Crash Recovery
Notes: In Fig. 5-30(a), the CPU crash happens before either copy of the block is written. During
recovery, neither will be changed and the old value will continue to exist, which is allowed.
In Fig. 5-30(b), the CPU crashes during the write to drive l, destroying the contents of the
block. However the recovery program detects this error and restores the block on drive 1
from drive 2. Thus the effect of the crash is wiped out and the old state is fully restored.
In Fig. 5-30(c), the CPU crash happens after drive 1 is written but before drive 2 is written.
The point of no return has been passed here: the recovery program copies the block from
drive 1 to drive 2. The write succeeds.
Fig. 5-30(d) is like Fig. 5-30(b): during recovery, the good block overwrites the bad block.
Again, the final value of both blocks is the new one.
Finally, in Fig. 5-30(e) the recovery program sees that both blocks are the same, so neither
is changed and the write succeeds here too.

## Slide 48
  If 10,000 rpm disk has 300 sectors per track of 512 bytes each and calculate the data rate?
  512*300 = 153600 bytes on a track
  Data rate = 153600*10000/60 = 25600000 bytes/sec
  = 24.4 MB/sec

## Slide 49
  A disk has 8 sectors per track and spins at 600 rpm. It takes the controller time 10ms from the end of one I/O operation before it can issue a subsequent one. How long does it take to read all 8 sectors using the following interleaving system?
  a) No interleaving
  b) Single interleaving
  c) Double interleaving
  http://www.urch.com/forums/gre-computer-science/6451-schaums-os-7-a.html
Notes: 60 secs ---- 600 rev
1 sec ---- 600/60 rev
1 sec ---- 10 rev
600 rev == 60 sec
1 rev == 60/600 sec
1 rev == (60/600)*1000 ms = 100 ms

## Slide 50
Suppose that a disk drive has 300 cylinders, numbered from 0 to 299. The drive is currently serving a request at cylinder 143 and the previous request was at cylinder 15. The queue of pending requests, in FIFO order, is 86, 147, 291, 18, 95, 151, 12, 175, 30. Starting from the current head position, what is the total distance(in cylinders) that the disk arm moves to satisfy all the pending requests for each of the following disk- scheduling algorithms?
FCFS ii) SSTF iii) SCAN iv) C-SCAN
v) LOOK vi) C-LOOK
Notes: 60 secs ---- 600 rev
1 sec ---- 600/60 rev
1 sec ---- 10 rev
600 rev == 60 sec
1 rev == 60/600 sec
1 rev == (60/600)*1000 ms = 100 ms

## Slide 51
CLOCKS & TERMINALS

## Slide 52
Two types of clock
  Simple clock: tied to 110 or 220 volt power line, causes an interrupt at every voltage cycle (50 or 60 Hz)
  Other type, used in modern computers based on crystal oscillator
    High accuracy, in the range of several hundred megahertz
    A programmable clock

## Slide 53
Programmable clocks
  Two modes: one-shot vs. square-wave
  In one-shot mode, when the clock is started, it copies the value of the holding register into the counter and then decrements the counter at each pulse from the crystal. When the counter gets to zero, it causes an interrupt and stops until it is explicitly started again by the software
  In square-wave mode, after getting to zero and causing the interrupt, the holding register is automatically copied into the counter, and the whole process is repeated again indefinitely
  Periodic interrupts are called “clock ticks”

## Slide 54
Common duties of clock software
  Maintaining the time of day
  Preventing processes from running longer than they are allowed to
  Accounting for CPU usage
  Handling the alarm system call made by user processes
  Providing watch-dog timers for parts of the system itself
  Doing profiling, monitoring and statistics gathering
Soft Timers
  Second programmable clock that can be set to cause timer interrupts at whatever rate a program needs

## Slide 55
Terminals
  A terminal is a device or a program that allows you to communicate with a computer system
  Can be a physical device, such as a keyboard and a monitor, or a software application, such as a terminal emulator